Hi John,

It isn't bad at all, in fact, it's a terrific system. You do need to either

borrow a bubble gauge from Baldwin (if they still do that), or buy one of

Tom Lowells (recommended). Below is a copy of Baldwin's supplied tech sheet

on the procedure, or you can phone Kent Webb for this, or any other

pertinent information. I have also included a chart for easy conversion

between the Baldwin, and Lowell gauge to make life easier for you. For those

who have seen this stuff, my apologies for the List posting. It has been a

year or so since I did this and I thought there might be enough new

listmates who haven't, for the rest of you to suffer the download.

--------------------- Page 1 -----------------------

1-29-1997

TS039D

PROCEDURE TO ESTABLISH PROPER DOWN BEARING OF STRINGS ON BRIDGES OF BALDWIN

GRAND  PIANOS DESIGNED WITH HOLLOW VERTICAL (ACU-JUST) HITCH PINS

These conditions must exist before bearing can be established:

1.All strings associated with the treble bridge must be in place,  (Bass

strings to be installed later.)

2.  These strings must be tuned to A-440 pitch.

3.  All strings on the treble bridge must be set at proper height on their

hitch pins to read zero (0.0) bearing at the bridge.  Follow this procedure;

begin at treble end of treble bridge with note #88 and work toward bass.

Lift wire and raise tension of the strings on the first ten (10) notes,

Then raise wire and adjust tension of the next ten (10) notes and proceed on

until all wire is adjusted in this manner on the treble bridge.

Procedure for string height adjustment.

1.  Become familiar with bubble gage adjustments and application as shown

with the attached illustrations,

2.  With strings at normal tension, begin with strings at the bass end of

the treble bridge and work toward the middle,  Set bearing values as shown

in the following chart on specified notes only.  Tap the string down by

placing the tool over the hitch pin, resting on the wire,  with the bubble

gage held onto proper strings with the magnet built into its base, tap the

setting tool with a small hammer to lower the string to achieve a proper

bubble gage reading.  If the string is too low, raise the string, using a

coil lifter and leather or felt to protect the plate finish.

Scale              SA(5'2")  ST(5'8")  SC(6'3'')  SF10(7'0")  SD10(9'0'')

Notes to be set    27-44     27-43     23-40      21-39       21-35

Bubble Deflection  1 divis.  1 divis.  1 divis.   1 divis.    1 divis.

3.  After strings associated with the notes which were adjusted in the

preceding operation have been set, proceed on with notes listed in the

following charts.

Scale              SA(5' 2")  ST(5'8")  SC(6'3'')  SF10(7'0")  SD10(9'0")

Notes to be set    45-53      44-53     41-53      40-53       36-53

Bubble Deflection  2 divis.   2 divis.  2 divis.   2 divis.    2 divis.

Scale              SA(5'2")   ST(5'8")  SC(6'3")   SF10(7'0")  SD10(9'0")

Notes to be set    54-88      54-88     54-88      54-88       54-88

Bubble Deflection  3 divis.   3 divis.  3 divis.   3 divis.    3 divis.

4,  Install bass strings and set at zero bearing,  Then adjust bearing

according to the following chart.

Scale              SA(5'2")  ST(5'8")  SC(6'3")  SF10(7'0")  SD10(9'0")

Notes to be set    1-26      1-26      1-20      1-20        1-20

Bubble Deflection  1 divis.  1 divis.  1 divis.  1 divis.    1 divis

5.   Retune piano to A-440 pitch.

CONCLUSION:

1. Bearing adjustments should only be made when the piano is maintained

under proper climatic conditions.  (Humidity 35% - 45% with temperature 70 -

75)

2. The procedure and bearing gage must be applied in the order established.

3. A bearing value, previously set, cannot be rechecked because the

accumulated force of all strings on the bridges will lower the soundboard

and reduce the settings which were originally set.

4. Pianos equipped with the vertical (Acu-Just) hitch pins are designed to

function with a minimum positive bearing at the bridges, compared with other

pianos with string rests and angled hitch pins.

*Hand written note at bottom: 1 div. = .005" shim thickness with a Baldwin

Rocker Gage.

------------------  Page 2 -----------------------------

Bubble reading to Degrees to Bearing Load conversion

for Lowell and Baldwin downbearing gauges.

Measure bubble offset difference between string segments

on both sides of the bridge. Look up angle and bearing factor

on appropriate chart. For bearing load in pounds, multiply

bearing factor times string tension.

Ron Nossaman July, 1997

Baldwin Gauge            |        Lowell Gauge

------------------------------|-----------------------------

Bubble Degrees   Bearing    |     Bubble Degrees   Bearing

------------------------------|-----------------------------

0.5    0.14167   0.0025     |     0.5    0.08333   0.0015

1.0    0.28333   0.005      |     1.0    0.16667   0.003

1.5    0.42499   0.0075     |     1.5    0.25      0.0045

2.0    0.56666   0.01       |     2.0    0.33333   0.006

2.5    0.70832   0.0125     |     2.5    0.41667   0.0075

3.0    0.84999   0.015      |     3.0    0.5       0.009

3.5    0.99165   0.0175     |     3.5    0.58333   0.0105

4.0    1.13332   0.02       |     4.0    0.66667   0.012

4.5    1.27499   0.0225     |     4.5    0.75      0.0135

5.0    1.41665   0.025      |     5.0    0.83333   0.015

5.5    1.55832   0.0275     |     5.5    0.91667   0.0165

6.0    1.69998   0.03       |     6.0    1.        0.018

6.5    1.84165   0.0325     |     6.5    1.08333   0.0195

7.0    1.98331   0.035      |     7.0    1.16667   0.021

7.5    2.12497   0.0375     |     7.5    1.25      0.0225

8.0    2.26664   0.04       |     8.0    1.33333   0.024

8.5    2.40831   0.0425     |     8.5    1.41667   0.0255

9.0    2.54997   0.045      |     9.0    1.5       0.027

9.5    2.69163   0.0475     |     9.5    1.58333   0.0285

10.0   2.8333    0.05       |     10.0   1.66667   0.03

10.5   2.97497   0.0525     |     10.5   1.75      0.0315

11.0   3.11663   0.055      |     11.0   1.83333   0.033

11.5   3.25829   0.0575     |     11.5   1.91667   0.0345

12.0   3.39996   0.06       |     12.0   2.        0.036

12.5   3.54163   0.0625     |     12.5   2.08333   0.0375

13.0   3.68329   0.065      |     13.0   2.16667   0.039

13.5   3.82496   0.0675     |     13.5   2.25      0.0405

14.0   3.96662   0.07       |     14.0   2.33333   0.042

14.5   4.10829   0.0725     |     14.5   2.41667   0.0435

15.0   4.24995   0.075      |     15.0   2.5       0.045

15.5   4.39162   0.0775     |     15.5   2.58333   0.0465

16.0   4.53328   0.08       |     16.0   2.66667   0.048

Ron

Bearing1.txt is from a Baldwin tech sheet, direct from the source.

Bearing4.txt is a conversion chart to relate the instructions in bearing1 to degrees, so you can use a Lowell gage, Wixey, or whatever, instead of Baldwin's gage.

Ron N

Bubble reading to Degrees to Bearing Load conversion

for Lowell and Baldwin downbearing gauges.

Measure bubble offset difference between string segments

on both sides of the bridge. Look up angle and bearing factor

on appropriate chart. For bearing load in pounds, multiply

bearing factor times string tension.

Ron Nossaman July, 1997

Baldwin Gauge            |        Lowell Gauge

------------------------------|-----------------------------

Bubble Degrees   Bearing    |     Bubble Degrees   Bearing

------------------------------|-----------------------------

0.5    0.14167   0.0025     |     0.5    0.08333   0.0015

1.0    0.28333   0.005      |     1.0    0.16667   0.003

1.5    0.42499   0.0075     |     1.5    0.25      0.0045

2.0    0.56666   0.01       |     2.0    0.33333   0.006

2.5    0.70832   0.0125     |     2.5    0.41667   0.0075

3.0    0.84999   0.015      |     3.0    0.5       0.009

3.5    0.99165   0.0175     |     3.5    0.58333   0.0105

4.0    1.13332   0.02       |     4.0    0.66667   0.012

4.5    1.27499   0.0225     |     4.5    0.75      0.0135

5.0    1.41665   0.025      |     5.0    0.83333   0.015

5.5    1.55832   0.0275     |     5.5    0.91667   0.0165

6.0    1.69998   0.03       |     6.0    1.        0.018

6.5    1.84165   0.0325     |     6.5    1.08333   0.0195

7.0    1.98331   0.035      |     7.0    1.16667   0.021

7.5    2.12497   0.0375     |     7.5    1.25      0.0225

8.0    2.26664   0.04       |     8.0    1.33333   0.024

8.5    2.40831   0.0425     |     8.5    1.41667   0.0255

9.0    2.54997   0.045      |     9.0    1.5       0.027

9.5    2.69163   0.0475     |     9.5    1.58333   0.0285

10.0   2.8333    0.05       |     10.0   1.66667   0.03

10.5   2.97497   0.0525     |     10.5   1.75      0.0315

11.0   3.11663   0.055      |     11.0   1.83333   0.033

11.5   3.25829   0.0575     |     11.5   1.91667   0.0345

12.0   3.39996   0.06       |     12.0   2.        0.036

12.5   3.54163   0.0625     |     12.5   2.08333   0.0375

13.0   3.68329   0.065      |     13.0   2.16667   0.039

13.5   3.82496   0.0675     |     13.5   2.25      0.0405

14.0   3.96662   0.07       |     14.0   2.33333   0.042

14.5   4.10829   0.0725     |     14.5   2.41667   0.0435

15.0   4.24995   0.075      |     15.0   2.5       0.045

15.5   4.39162   0.0775     |     15.5   2.58333   0.0465

16.0   4.53328   0.08       |     16.0   2.66667   0.048

1-29-1997                                                                                      TS039D

PROCEDURE TO ESTABLISH PROPER DOWN BEARING OF STRINGS ON BRIDGES OF BALDWIN GRAND  PIANOS DESLGNED WITH HOLLOW VERTICAL (ACU-JUST) HITCH PINS

These conditions must exist before bearing can be established:

1.All strings associated with the treble bridge must be in place,  (Bass strings to be installed later.)

2.  These strings must be tuned to A-440 pitch.

3.  All strings on the treble bridge must be set at proper height on their hitch pins to read zero (0.0) bearing at the bridge.  Follow this procedure; begin at treble end of treble bridge with note #88 and work toward bass.  Lift wire and raise tension of the strings on the first ten (10) notes,  Then raise wire and adjust tension of the next ten (10) notes and proceed on until all wire is adjusted in this manner on the treble bridge.

Procedure for string height adjustment.

1.  Become familiar with bubble gage adjustments and application as shown with the attached illustrations,

2.  With strings at normal tension, begin with strings at the bass end of the treble bridge and work toward the middle,  Set bearing values as shown in the following chart on specified notes only.  Tap the string down by placing the tool over the hitch pin, resting on the wire,  with the bubble gage held onto proper strings with the magnet built into its base, tap the setting tool with a small hammer to lower the string to achieve a proper bubble gage reading.  If the string is too low, raise the string, using a coil lifter and leather or felt to protect the plate finish.

Scale                      SA(5'2")    ST(5'8")    SC(6'3'')    SF10(7'0")    SD10(9'0'')

Notes to be set            27-44       27-43       23-40        21-39           21-35

Bubble Deflection          1 divis.    1 divis.    1 divis.     1 divis.         1 divis.

3.  After strings associated with the notes which were adjusted in the preceding operation have been set, proceed on with notes listed in the following charts.

Scale                      SA(5' 2")   ST(5'8")    SC(6'3'')    SF10(7'0")     SD10(9'0")

Notes to be set            45-53       44-53       41-53        40-53          36-53

Bubble Deflection          2 divis.    2 divis.    2 divis.     2 divis.       2 divis.

Scale                      SA(5'2")    ST(5'8")    SC(6'3")     SF10(7'0")     SD10(9'0")

Notes to be set            54-88       54-88       54-88        54-88             54-88

Bubble Deflection          3 divis.    3 divis.    3 divis.     3 divis.            3 divis.

4,  Install bass strings and set at zero bearing,  Then adjust bearing according to the following chart.

Scale                      SA(5'2")    ST(5'8")    SC(6'3")     SF10(7'0")     SD10(9'0")

Notes to be set            1-26        1-26        1-20         1-20               1-20

Bubble Deflection          1 divis.    1 divis.    1 divis.     1 divis.           1 divis

5.   Retune piano to A-440 pitch.

CONCLUSION:

1. Bearing adjustments should only be made when the piano is maintained under proper climatic conditions.  (Humidity 35% - 45% with temperature 70 - 75)

2. The procedure and bearing gage must be applied in the order established.

3. A bearing value, previously set, cannot be rechecked because the accumulated force of all strings on the bridges will lower the soundboard and reduce the settings which were originally set.

4. Pianos equipped with the vertical (Acu-Just) hitch pins are designed to function with a minimum positive bearing at the bridges, compared with other pianos with string rests and angled hitch pins.

*Hand written note at bottom: 1 div. = .005" shim thickness with a Baldwin Rocker Gage.